## Slide 1: FreeRTOS Simulation on Linux
Hossein Assaran

## Slide 2: About Me
B.S. in Electrical Engineering: Shahed University
M.A. in Philosophy
Over 10 Years in Embedded System Design and Development
  AVR, PIC ,ARM9, ARM7, CORTEX-M0, CORTEX-M3, CORTEX-M4, CORTEX-A5, CORTEX-A8
Startup Owner: Fibook, Khanebazia, Cpuban, Filink, Lernino, …
Linux
FreeRTOS
Kotlin
GitHub: https://github.com/HosseinAssaran

## Slide 3: Resources
Hands-On RTOS With Microcontrollers
Brian Amos
Mastering the FreeRTOS™ Real Time Kernel
Richard Barry
FreeRTOS.org

## Slide 4: What is Real-Time?
Any system that has a deterministic response to a given event can be considered "real-time."

## Slide 5: Types Of Real Time Systems
Hardware
Bare-metal firmware
RTOS-based firmware
RTOS-based software
Carefully crafted OS software

## Slide 6: What is Jitter?

## Slide 7: What is FreeRTOS?
A lightweight, open-source real-time operating system for microcontrollers
Designed for embedded systems with limited resources
Compiled and linked directly with the application code

## Slide 8: Bare Metal, Linux RT, and FreeRTOS – Ease of Use
Bare Metal | Linux RT | FreeRTOS
Low-Level Control | Familiar Environment | Modular Design
High Complexity | More Complex Setup and Configuration | Simpler Learning Carve And Easier To Setup Compared To Linux
More Development Time | Rich Ecosystem | Comprehensive Documentation

## Slide 9: Bare Metal, Linux RT, and FreeRTOS – Performance and Resource Management
Bare Metal | Linux RT | FreeRTOS
Maximum Performance | Low Performance | Balanced Performance
Minimal Overhead | Higher Resource Demands - Requiring A Microprocessor With At Least 300mhz Speed | Efficient Resource Management
Smallest Footprint | A Kernel Size That Cannot Be Reduced Below Several Hundred Kilobytes | Minimal Footprint - RTOS Kernel Itself Required About 5 To 10 Kbytes Of ROM Space

## Slide 10: Bare Metal, Linux RT, and FreeRTOS – Flexibility and Scalability
Bare Metal | Linux RT | FreeRTOS
High Flexibility | Highly Configurable | Modular And Portable
Limited Scalability, Typically Used For Very Specific Applications | Highly Scalable From Embedded Systems To Large Servers | Scalable For Small To Medium Embedded Systems

## Slide 11: Bare Metal, Linux RT, and FreeRTOS – Use Case
Bare Metal | Linux RT | FreeRTOS
Suitable For Low-level System Development, Firmware, And Performance-critical Applications - Microcontroller-based applications, high-performance computing tasks, and real-time signal processing | Ideal For Complex Systems Requiring Both Real-time Performance And The Rich Features Of A General-purpose OS. Automotive systems, industrial automation, telecommunications, and mission-critical infrastructure. | Best For Embedded Systems With Real-time Requirements And Constrained Resources. IoT devices, consumer electronics, medical devices, and industrial control systems.

## Slide 12: Why Simulate FreeRTOS on Linux?
Faster development cycles without the need for physical hardware.
Easier debugging and testing
Cost-effective and convenient
Ability to quickly iterate and test changes
Speeding Up Development Cycles

## Slide 13: Setting Up FreeRTOS Simulation on Linux
Installing necessary software and tools
  QEMU For Virtualization
  GCC For Compiling
  GDB For Debugging
Complete Guide on:
  https://github.com/HosseinAssaran/FreeRTOS_Examples

## Slide 14: Let’s Do It